## Slide 1
Chapter 5
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Chapter 5 :: Topics
Introduction
Arithmetic Circuits
Number Systems
Sequential Building Blocks
Memory Arrays
Logic Arrays

## Slide 3
Digital building blocks:
  Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays
Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components
  Well-defined interfaces and functions
  Regular structure easily extends to different sizes
Will use these building blocks in Chapter 7 to build microprocessor
Introduction

## Slide 4
1-Bit Adders

## Slide 5
Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware
Symbol
Multibit Adders (CPAs)

## Slide 6
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow
Ripple-Carry Adder

## Slide 7
tripple = NtFA
where tFA is the delay of a 1-bit full adder
Ripple-Carry Adder Delay

## Slide 8
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Generate: Column i will generate a carry out if Ai and Bi are both 1.
  Gi = Ai Bi
    Propagate: Column i will propagate a carry in to the carry out if Ai or Bi is 1.
  Pi = Ai + Bi
    Carry out: The carry out of column i (Ci) is:
  Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1
Carry-Lookahead Adder

## Slide 9
Now use column Propagate and Generate signals to compute Block Propagate and Generate signals for k-bit blocks, i.e.:
  Compute if a k-bit group will propagate a carry in (to the block) to the carry out (of the block)
  Compute if a k-bit group will generate a carry out (of the block)
Block Propagate and Generate

## Slide 10
Example: Block propagate and generate signals for 4-bit blocks (P3:0 and G3:0):
  P3:0 = P3P2 P1P0
  G3:0 = G3 + G2P3 + G1P2P3 + G0P1P2P3
  = G3 + P3 (G2 + P2 (G1 + P1G0 )
Block Propagate and Generate Signals

## Slide 11
In general for a block spanning bits i through j,
  Pi:j = PiPi-1 Pi-2 … Pj
  Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2 … Gj )
  Ci = Gi:j + Pi:j Cj-1
Block Propagate and Generate Signals

## Slide 12
32-bit CLA with 4-bit Blocks

## Slide 13
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate logic (meanwhile computing sums)
Step 4: Compute sum for most significant k-bit block
Carry-Lookahead Addition

## Slide 14
Step 1: Compute Gi and Pi for all columns
Carry-Lookahead Addition
  Gi = Ai Bi
  Pi = Ai + Bi

## Slide 15
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Carry-Lookahead Addition
  P3:0 = P3P2 P1P0
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 )

## Slide 16
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate logic (meanwhile computing sums)
Carry-Lookahead Addition
A
3:0
B
3:0
S
3:0
4-bit CLA
Block
C
in
A
7:4
B
7:4
S
7:4
4-bit CLA
Block
C
3
C
7
A
27:24
B
27:24
S
27:24
4-bit CLA
Block
C
23
A
31:28
B
31:28
S
31:28
4-bit CLA
Block
C
27
C
out
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in

## Slide 17
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate logic (meanwhile computing sums)
Step 4: Compute sum for most significant k-bit block
Carry-Lookahead Addition
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in

## Slide 18
For N-bit CLA with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
  tpg : delay to generate all Pi, Gi
  tpg_block : delay to generate all Pi:j, Gi:j
  tAND_OR : delay from Cin to Cout of final AND/OR gate in k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16
Carry-Lookahead Adder Delay

## Slide 19
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai ^ Bi) ^ Ci-1
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
log2N stages
Prefix Adder

## Slide 20
Carry in either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
  G-1 = Cin
Carry in to column i = carry out of column i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
  Si = (Ai ^ Bi) ^ Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes) (= C0, C1, C2, C3, C4, C5, …)
Prefix Adder

## Slide 21
Generate and propagate signals for a block spanning bits i:j
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words:
  Generate: block i:j will generate a carry if:
    upper part (i:k) generates a carry or
    upper part (i:k) propagates a carry generated in lower part (k-1:j)
  Propagate: block i:j will propagate a carry if both the upper and lower parts propagate the carry
Prefix Adder

## Slide 22
16-Bit Prefix Adder Schematic
0:-1
-1
2:1
1:-1
2:-1
0
1
2
4:3
3
6:5
5:3
6:3
4
5
6
5:-1
6:-1
3:-1
4:-1
8:7
7
10:9
9:7
10:7
8
9
10
12:11
11
14:13
13:11
14:11
12
13
14
13:7
14:7
11:7
12:7
9:-1
10:-1
7:-1
8:-1
13:-1
14:-1
11:-1
12:-1
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
G
k-1:j
P
k-1:j
G
i:k
P
i:k
G
i:j
P
i:j
B
i
A
i
G
i:i
P
i:i
i
i:j
B
i
A
i
G
i-1:-1
S
i
i

## Slide 23
tPA = tpg + log2N(tpg_prefix ) + tXOR
  tpg: delay to produce Pi, Gi (AND or OR gate)
  tpg_prefix: delay of black prefix cell (AND-OR gate)
Prefix Adder Delay

## Slide 24
Compare delay of: 32-bit ripple-carry, CLA, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 10 ps; full adder delay = 30 ps
tripple = NtFA = 32(30 ps)
= 960 ps
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [10 + 60 + (7)20 + 4(30)] ps
= 330 ps
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [10 + log232(20) + 10] ps
= 120 ps
Adder Delay Comparisons

## Slide 25
Subtracter

## Slide 26
Comparator: Equality

## Slide 27
Comparator: Less Than

## Slide 28
ALU should perform:
Addition
Subtraction
AND
OR
ALU: Arithmetic Logic Unit

## Slide 29
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl = 00
Result = A + B

## Slide 30
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B

## Slide 31
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B
ALUControl1:0 = 11
Mux selects output of OR gate as Result, so
Result = A OR B

## Slide 32
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B

## Slide 33
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl1:0 = 00
ALUControl0 = 0, so:
Cin to adder = 0
2nd input to adder is B
Mux selects Sum as Result, so
Result = A + B

## Slide 34
Flag | Description
N | Result is Negative
Z | Result is Zero
C | Adder produces Carry out
V | Adder oVerflowed
ALU with Status Flags

## Slide 35
ALU with Status Flags

## Slide 36
ALU with Status Flags: Negative
N = 1 if:
Result is negative
So, N is connected to most significant bit of Result

## Slide 37
ALU with Status Flags: Zero
Z = 1 if:
all of the bits of Result are 0

## Slide 38
ALU with Status Flags: Carry
C = 1 if:
Cout of Adder is 1
AND
ALU is adding or subtracting (ALUControl is 00 or 01)

## Slide 39
ALU with Status Flags: oVerflow
V = 1 if:
The addition of 2 same-signed numbers produces a result with the opposite sign

## Slide 40
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)

## Slide 41
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs

## Slide 42
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs
AND
A and B have same signs upon addition OR
A and B have different signs upon subtraction

## Slide 43
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs
AND
A and B have same signs upon addition (ALUControl0 = 0) OR
A and B have different signs upon subtraction
(ALUControl0 = 1)

## Slide 44
Multiplexers
Decoders
Combinational Building Blocks

## Slide 45
Selects between one of N inputs to connect to output
log2N-bit select input – control input
Example: 2:1 Mux
Multiplexer (Mux)

## Slide 46
Logic gates
  Sum-of-products form
Tristates
  For an N-input mux, use N tristates
  Turn on exactly one to select the appropriate input
Multiplexer Implementations

## Slide 47
Using mux as a lookup table
Logic using Multiplexers

## Slide 48
Reducing the size of the mux
Logic using Multiplexers

## Slide 49
Reducing the size of the mux
Logic using Multiplexers

## Slide 50
Reducing the size of the mux
Logic using Multiplexers

## Slide 51
Reducing the size of the mux
Logic using Multiplexers

## Slide 52
N inputs, 2N outputs
One-hot outputs: only one output HIGH at once
Decoders

## Slide 53
Decoder Implementation

## Slide 54
OR minterms
Logic Using Decoders

## Slide 55
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb)
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111
Shifters

## Slide 56
Shifter Design

## Slide 57
Shifter Design
= A3
= A2
= A1
= A0

## Slide 58
Shifter Design
= 0
= A3
= A2
= A1

## Slide 59
Shifter Design
= 0
= 0
= A3
= A2

## Slide 60
Shifter Design
= 0
= 0
= 0
= A3

## Slide 61
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 62
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 63
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 64
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 65
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 66
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 67
4 x 4 Multiplier

## Slide 68
4 x 4 Multiplier

## Slide 69
4 x 4 Multiplier

## Slide 70
4 x 4 Multiplier

## Slide 71
4 x 4 Multiplier

## Slide 72
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Dividers

## Slide 73
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Long-Hand:
Dividers

## Slide 74
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Long-Hand:
Dividers
Long-Hand Revisited:

## Slide 75
A/B = Q + R/B
Decimal: 2584/15 = 172 R4
Dividers
Binary: 1101/0010 = 0110 R1

## Slide 76
Divider Algorithm
A/B = Q + R/B
R’ = 0
for i = N-1 to 0
R = {R’ << 1, Ai}
D = R - B
if D < 0, Qi= 0; R’= R
else Qi= 1; R’= D
R=R’
Binary: 1101/10 = 0110 R1

## Slide 77
4 x 4 Divider
Division: A/B = Q + R/B
R’ = 0
for i = N-1 to 0
R = {R’ << 1, Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R=R’
Each row computes one iteration of the division algorithm.

## Slide 78
4 x 4 Divider
Each row computes one iteration of the division algorithm.

## Slide 79
4 x 4 Divider
Each row computes one iteration of the division algorithm.

## Slide 80
4 x 4 Divider
Each row computes one iteration of the division algorithm.

## Slide 81
4 x 4 Divider
Each row computes one iteration of the division algorithm.

## Slide 82
4 x 4 Divider
Each row computes one iteration of the division algorithm.

## Slide 83
4 x 4 Divider Ej.: 1101(A)/0010(B)
Division: A/B = Q + R/B
R’ = 0
for i = N-1 to 0
R = {R’ << 1, Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R=R’
1
1
1
0
1
1
0
0
1
1
1
0
0
0
1
1
1
1
1
1
1
1
1
0
0
0
1
1
1
1
0
0
1
1
0
1
0
0
0
1
1
0
1
1
1
1
0
0
1
1
1
1
1
0
0
0

## Slide 84
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/ written at each unique N-bit address
Memory Arrays

## Slide 85
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M
Memory Arrays

## Slide 86
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100
Memory Array Example

## Slide 87
Memory Arrays

## Slide 88
Random access memory (RAM): volatile
Read only memory (ROM): nonvolatile
Types of Memory

## Slide 89
Volatile: loses its data when power off
Read and written quickly
Main memory in your computer is RAM (DRAM)
Historically called random access memory because any data word accessed as easily as any other (in contrast to sequential access memories such as a tape recorder)
RAM: Random Access Memory

## Slide 90
Nonvolatile: retains data when power off
Read quickly, but writing is impossible or slow
Flash memory in cameras, thumb drives, and digital cameras are all ROMs
  Historically called read only memory because ROMs were written at manufacturing time or by burning fuses. Once ROM was configured, it could not be written again. This is no longer the case for Flash memory and other types of ROMs.
ROM: Read Only Memory

## Slide 91
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters
Types of RAM

## Slide 92
Chapter 5
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris