## Slide 1
Chapter 7
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Chapter 7 :: Topics
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Advanced Microarchitecture

## Slide 3
Microarchitecture: how to implement an architecture in hardware
Processor:
  Datapath: functional blocks
  Control: control signals
Introduction

## Slide 4
Multiple implementations for a single architecture:
  Single-cycle: Each instruction executes in a single cycle
  Multicycle: Each instruction is broken up into series of shorter steps
  Pipelined: Each instruction broken up into series of steps & multiple instructions execute at once
Microarchitecture

## Slide 5
Program execution time
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
Definitions:
  CPI: Cycles/instruction
  clock period: seconds/cycle
  IPC: instructions/cycle = IPC
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance
Processor Performance

## Slide 6
Consider subset of ARM instructions:
  Data-processing instructions:
    ADD, SUB, AND, ORR
    with register and immediate Src2, but no shifts
  Memory instructions:
    LDR, STR
    with positive immediate offset
  Branch instructions:
    B
ARM Processor

## Slide 7
Determines everything about a processor:
  Architectural state:
    16 registers (including PC)
    Status register
  Memory
Architectural State Elements

## Slide 8
ARM Architectural State Elements

## Slide 9
Datapath
Control
Single-Cycle ARM Processor

## Slide 10
Datapath
Control
Single-Cycle ARM Processor

## Slide 11
Datapath: start with LDR instruction
Example: LDR R1, [R2, #5]
LDR Rd, [Rn, imm12]
Single-Cycle ARM Processor

## Slide 12
STEP 1: Fetch instruction
Single-Cycle Datapath: LDR fetch

## Slide 13
STEP 2: Read source operands from RF
Single-Cycle Datapath: LDR Reg Read
LDR Rd, [Rn, imm12]

## Slide 14
STEP 3: Extend the immediate
Single-Cycle Datapath: LDR Immed.
LDR Rd, [Rn, imm12]

## Slide 15
STEP 4: Compute the memory address
Single-Cycle Datapath: LDR Address
LDR Rd, [Rn, imm12]

## Slide 16
LDR Rd, [Rn, imm12]
STEP 5: Read data from memory and write it back to register file
Single-Cycle Datapath: LDR Mem Read

## Slide 17
STEP 6: Determine address of next instruction
Single-Cycle Datapath: PC Increment

## Slide 18
PC can be source/destination of instruction
Single-Cycle Datapath: Access to PC

## Slide 19
PC can be source/destination of instruction
Source: R15 must be available in Register File
  PC is read as the current PC plus 8
Single-Cycle Datapath: Access to PC

## Slide 20
PC can be source/destination of instruction
Source: R15 must be available in Register File
  PC is read as the current PC plus 8
Destination: Be able to write result to PC
Single-Cycle Datapath: Access to PC

## Slide 21
Expand datapath to handle STR:
Write data in Rd to memory
Single-Cycle Datapath: STR
STR Rd, [Rn, imm12]

## Slide 22
With immediate Src2:
Read from Rn and Imm8 (ImmSrc chooses the zero-extended Imm8 instead of Imm12)
Write ALUResult to register file
Write to Rd
Single-Cycle Datapath: Data-processing
ADD Rd, Rn, imm8

## Slide 23
With immediate Src2:
Read from Rn and Imm8 (ImmSrc chooses the zero-extended Imm8 instead of Imm12)
Write ALUResult to register file
Write to Rd
Single-Cycle Datapath: Data-processing
ADD Rd, Rn, imm8

## Slide 24
With register Src2:
Read from Rn and Rm (instead of Imm8)
Write ALUResult to register file
Write to Rd
Single-Cycle Datapath: Data-processing
ADD Rd, Rn, Rm

## Slide 25
With register Src2:
Read from Rn and Rm (instead of Imm8)
Write ALUResult to register file
Write to Rd
Single-Cycle Datapath: Data-processing
ADD Rd, Rn, Rm

## Slide 26
Calculate branch target address:
BTA = (ExtImm) + (PC + 8)
ExtImm = Imm24 << 2 and sign-extended
Single-Cycle Datapath: B
B Label

## Slide 27
Single-Cycle Datapath: ExtImm
ImmSrc1:0 | ExtImm | Description
00 | {24’b0, Instr7:0} | Zero-extended imm8
01 | {20’b0, Instr11:0} | Zero-extended imm12
10 | {6{Instr23}, Instr23:0} | Sign-extended imm24

## Slide 28
Single-Cycle ARM Processor

## Slide 29
Single-Cycle Control

## Slide 30
Single-Cycle Control
Sent directly
to datapath

## Slide 31
Single-Cycle Control
Sent through
Conditional Logic
first, then to
datapath
Sent directly
to datapath

## Slide 32
Single-Cycle Control
These signals change the state (PC, RF, Memory)
If instruction shouldn’t execute, forced to 0
Sent through
Conditional Logic
first, then to
datapath
Sent directly
to datapath

## Slide 33
Single-Cycle Control
FlagW1:0: Flag Write signal, asserted when ALUFlags should be saved (i.e., on instruction with S=1)

## Slide 34
Single-Cycle Control
FlagW1:0: Flag Write signal, asserted when ALUFlags should be saved (i.e., on instruction with S=1)
ADD, SUB update all flags (NZCV)
AND, ORR only update NZ flags

## Slide 35
Single-Cycle Control
FlagW1:0: Flag Write signal, asserted when ALUFlags should be saved (i.e., on instruction with S=1)
ADD, SUB update all flags (NZCV)
AND, ORR only update NZ flags
So, two bits needed:
  FlagW1 = 1: NZ saved (ALUFlags3:2 saved)
  FlagW0 = 1: CV saved (ALUFlags1:0 saved)

## Slide 36
Single-Cycle Control

## Slide 37
Single-Cycle Control: Decoder

## Slide 38
Submodules:
Main Decoder
ALU Decoder
PC Logic
Single-Cycle Control: Decoder

## Slide 39
Submodules:
Main Decoder
ALU Decoder
PC Logic
Single-Cycle Control: Decoder

## Slide 40
Op | Funct5 | Funct0 | Type | Branch | MemtoReg | MemW | ALUSrc | ImmSrc | RegW | RegSrc | ALUOp
00 | 0 | X | DP Reg | 0 | 0 | 0 | 0 | XX | 1 | 00 | 1
00 | 1 | X | DP Imm | 0 | 0 | 0 | 1 | 00 | 1 | X0 | 1
01 | X | 0 | STR | 0 | X | 1 | 1 | 01 | 0 | 10 | 0
01 | X | 1 | LDR | 0 | 1 | 0 | 1 | 01 | 1 | X0 | 0
10 | X | X | B | 1 | 0 | 0 | 1 | 10 | 0 | X1 | 0
Control Unit: Main Decoder

## Slide 41
Single-Cycle Control: Decoder
Submodules:
Main Decoder
ALU Decoder
PC Logic

## Slide 42
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Review: ALU

## Slide 43
Review: ALU

## Slide 44
Single-Cycle Control: Decoder
Submodules:
Main Decoder
ALU Decoder
PC Logic

## Slide 45
ALUOp | Funct4:1 (cmd) | Funct0 (S) | Type | ALUControl1:0 | FlagW1:0
0 | X | X | Not DP | 00 | 00
1 | 0100 | 0 | ADD | 00 | 00
 |  | 1 |  |  | 11
 | 0010 | 0 | SUB | 01 | 00
 |  | 1 |  |  | 11
 | 0000 | 0 | AND | 10 | 00
 |  | 1 |  |  | 10
 | 1100 | 0 | ORR | 11 | 00
 |  | 1 |  |  | 10
Control Unit: ALU Decoder
  FlagW1 = 1: NZ (Flags3:2) should be saved
  FlagW0 = 1: CV (Flags1:0) should be saved

## Slide 46
Single-Cycle Control: Decoder
Submodules:
Main Decoder
ALU Decoder
PC Logic

## Slide 47
PCS = 1 if PC is written by an instruction or branch (B):
PCS = ((Rd == 15) & RegW) | Branch
Single-Cycle Control: PC Logic
If instruction is executed: PCSrc = PCS
Else PCSrc = 0 (i.e., PC = PC + 4)

## Slide 48
Single-Cycle Control

## Slide 49
Single-Cycle Control: Cond. Logic

## Slide 50
Conditional Logic
Function:
Check if instruction should execute (if not, force PCSrc, RegWrite, and MemWrite to 0)
Possibly update Status Register (Flags3:0)

## Slide 51
Conditional Logic
Function:
Check if instruction should execute (if not, force PCSrc, RegWrite, and MemWrite to 0)
Possibly update Status Register (Flags3:0)

## Slide 52
Single-Cycle Control: Conditional Logic

## Slide 53
Conditional Logic: Conditional Execution
Depending on condition mnemonic (Cond3:0) and condition flags (Flags3:0) the instruction is executed (CondEx = 1)

## Slide 54
Depending on condition mnemonic (Cond3:0) and condition flags (Flags3:0) the instruction is executed (CondEx = 1)
Flags3:0 is the status register
Conditional Logic: Conditional Execution

## Slide 55
Review: Condition Mnemonics

## Slide 56
Example: AND R1, R2, R3
Cond3:0=1110 (unconditional) => CondEx = 1
Flags3:0 = NZCV
Conditional Logic: Conditional Execution

## Slide 57
Example: EOREQ R5, R6, R7
Cond3:0=0000 (EQ): if Flags = x1xx => CondEx = 1
Flags3:0 = NZCV
Conditional Logic: Conditional Execution

## Slide 58
Conditional Logic
Function:
Check if instruction should execute (if not, force PCSrc, RegWrite, and MemWrite to 0)
Possibly update Status Register (Flags3:0)

## Slide 59
Flags3:0 updated (with ALUFlags3:0) if:
FlagW is 1 (i.e., the instruction’s S-bit is 1) AND
CondEx is 1 (the instruction should be executed)
Flags3:0 = NZCV
Conditional Logic: Update (Set) Flags

## Slide 60
Recall:
ADD, SUB update all Flags
AND, OR update NZ only
So Flags status register has two write enables: FlagW1:0
Conditional Logic: Update (Set) Flags

## Slide 61
ALUOp | Funct4:1 (cmd) | Funct0 (S) | Type | ALUControl1:0 | FlagW1:0
0 | X | X | Not DP | 00 | 00
1 | 0100 | 0 | ADD | 00 | 00
 |  | 1 |  |  | 11
 | 0010 | 0 | SUB | 01 | 00
 |  | 1 |  |  | 11
 | 0000 | 0 | AND | 10 | 00
 |  | 1 |  |  | 10
 | 1100 | 0 | ORR | 11 | 00
 |  | 1 |  |  | 10
Review: ALU Decoder
  FlagW1 = 1: NZ (Flags3:2) should be saved
  FlagW0 = 1: CV (Flags1:0) should be saved

## Slide 62
Conditional Logic: Update (Set) Flags
All Flags updated
Example: SUBS R5, R6, R7
FlagW1:0 = 11 AND CondEx = 1 (unconditional) => FlagWrite1:0 = 11

## Slide 63
Conditional Logic: Update (Set) Flags
Flags3:0 = NZCV
Only Flags3:2 updated
i.e., only NZ Flags updated
Example: ANDS R7, R1, R3
FlagW1:0 = 10 AND CondEx = 1 (unconditional) => FlagWrite1:0 = 10

## Slide 64
Example: ORR
Op | Funct5 | Funct0 | Type | Branch | MemtoReg | MemW | ALUSrc | ImmSrc | RegW | RegSrc | ALUOp
00 | 0 | X | DP Reg | 0 | 0 | 0 | 0 | XX | 1 | 00 | 1

## Slide 65
Example: ORR

## Slide 66
Extended Functionality: CMP

## Slide 67
Extended Functionality: CMP
No change to datapath

## Slide 68
Extended Functionality: CMP

## Slide 69
Extended Functionality: CMP
ALUOp | Funct4:1 (cmd) | Funct0 (S) | Type | ALUControl1:0 | FlagW1:0 | NoWrite
0 | X | X | Not DP | 00 | 00 | 0
1 | 0100 | 0 | ADD | 00 | 00 | 0
 |  | 1 |  |  | 11 | 0
 | 0010 | 0 | SUB | 01 | 00 | 0
 |  | 1 |  |  | 11 | 0
 | 0000 | 0 | AND | 10 | 00 | 0
 |  | 1 |  |  | 10 | 0
 | 1100 | 0 | ORR | 11 | 00 | 0
 |  | 1 |  |  | 10 | 0
 | 1010 | 1 | CMP | 01 | 11 | 1

## Slide 70
Extended Functionality: Shifted Register

## Slide 71
No change to controller
Extended Functionality: Shifted Register

## Slide 72
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC
Review: Processor Performance

## Slide 73
TC limited by critical path (LDR)
Single-Cycle Performance

## Slide 74
Single-cycle critical path:
Tc1 = tpcq_PC + tmem + tdec +
max[tmux + tRFread, tsext + tmux] +
tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  Tc1 = tpcq_PC + 2tmem + tdec + tRFread + tALU + 2tmux + tRFsetup
Single-Cycle Performance

## Slide 75
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC

## Slide 76
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem

## Slide 77
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem
tdec

## Slide 78
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem
tdec
tmux + tRFread

## Slide 79
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem
tdec
tmux + tRFread
tsext + tmux

## Slide 80
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem
tdec
tmux + tRFread
tsext + tmux

## Slide 81
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem
tdec
tmux + tRFread
tsext + tmux
tALU

## Slide 82
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem
tdec
tmux + tRFread
tsext + tmux
tALU
tmem

## Slide 83
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem
tdec
tmux + tRFread
tsext + tmux
tALU
tmem
tmux

## Slide 84
TC limited by critical path (LDR)
Single-Cycle Performance
tpcq_PC
tmem
tdec
tmux + tRFread
tsext + tmux
tALU
tmem
tmux
tRFsetup

## Slide 85
Single-cycle critical path:
Tc1 = tpcq_PC + tmem + tdec +
max[tmux + tRFread, tsext + tmux] +
tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  Tc1 = tpcq_PC + 2tmem + tdec + tRFread + tALU + 2tmux + tRFsetup
Single-Cycle Performance

## Slide 86
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Decoder | tdec | 70
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60
  Tc1 = ?
Single-Cycle Performance Example

## Slide 87
  Tc1 = tpcq_PC + 2tmem + tdec + tRFread + tALU + 2tmux + tRFsetup
= [40 + 2(200) + 70 + 100 + 120 + 2(25) + 60] ps
= 840 ps
Single-Cycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Decoder | tdec | 70
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 88
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(840 × 10-12 s)
= 84 seconds
Single-Cycle Performance Example

## Slide 89
Single-cycle:
  + simple
  cycle time limited by longest instruction (LDR)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle processor addresses these issues by breaking instruction into shorter steps
  shorter instructions take fewer steps
  can re-use hardware
  cycle time is faster
Multicycle ARM Processor

## Slide 90
Single-cycle:
  + simple
  cycle time limited by longest instruction (LDR)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Multicycle ARM Processor

## Slide 91
Single-cycle:
  + simple
  cycle time limited by longest instruction (LDR)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Multicycle ARM Processor
Same design steps as single-cycle:
first datapath
then control

## Slide 92
Replace Instruction and Data memories with a single unified memory – more realistic
Multicycle State Elements

## Slide 93
STEP 1: Fetch instruction
Multicycle Datapath: Instruction Fetch
LDR Rd, [Rn, imm12]

## Slide 94
LDR Rd, [Rn, imm12]
Multicycle Datapath: LDR Register Read
STEP 2: Read source operands from RF

## Slide 95
LDR Rd, [Rn, imm12]
Multicycle Datapath: LDR Address
STEP 3: Compute the memory address

## Slide 96
LDR Rd, [Rn, imm12]
Multicycle Datapath: LDR Memory Read
STEP 4: Read data from memory

## Slide 97
LDR Rd, [Rn, imm12]
Multicycle Datapath: LDR Write Register
STEP 5: Write data back to register file

## Slide 98
Multicycle Datapath: Increment PC
Meanwhile: Increment PC
Concurrent with fetching instruction

## Slide 99
Multicycle Datapath: Access to PC
PC can be read/written by instruction

## Slide 100
Multicycle Datapath: Access to PC
PC can be read/written by instruction
Read: R15 (PC+8) available in Register File

## Slide 101
Multicycle Datapath: Read to PC (R15)
Example: ADD R1, R15, R2

## Slide 102
Multicycle Datapath: Read to PC (R15)
Example: ADD R1, R15, R2
R15 needs to be read as PC+8 from Register File (RF) in 2nd step
PC+4 was computed in 1st step
So (also in 2nd step) ALU computes (PC+4) + 4 for R15 input

## Slide 103
Multicycle Datapath: Read to PC (R15)
Example: ADD R1, R15, R2
R15 needs to be read as PC+8 from Register File (RF) in 2nd step
PC+4 was computed in 1st step
So (also in 2nd step) ALU computes (PC+4) + 4 for R15 input
  SrcA = PC (which was already updated in step 1 to PC+4)
  SrcB = 4
  ALUResult = PC + 8
ALUResult is fed to R15 input port of RF in 2nd step (which is then routed to RD1 output of RF)

## Slide 104
Multicycle Datapath: Access to PC
PC can be read/written by instruction
Read: R15 (PC+8) available in Register File
Write: Be able to write result of instruction to PC

## Slide 105
Multicycle Datapath: Write to PC (R15)
Example: SUB R15, R8, R3

## Slide 106
Multicycle Datapath: Write to PC (R15)
Example: SUB R15, R8, R3
Result of instruction needs to be written to the PC register
ALUResult already routed to the PC register, just assert PCWrite

## Slide 107
Multicycle Datapath: Write to PC (R15)
Example: SUB R15, R8, R3
Result of instruction needs to be written to the PC register
ALUResult already routed to the PC register, just assert PCWrite

## Slide 108
Write data in Rn to memory
Multicycle Datapath: STR

## Slide 109
With immediate addressing (i.e., an immediate Src2), no additional changes needed for datapath
Multicycle Datapath: Data-processing

## Slide 110
With register addressing (register Src2):
Read from Rn and Rm
Multicycle Datapath: Data-processing

## Slide 111
Calculate branch target address:
BTA = (ExtImm) + (PC+8)
ExtImm = Imm24 << 2 and sign-extended
Multicycle Datapath: B

## Slide 112
Multicycle ARM Processor

## Slide 113
Multicycle Control
First, discuss Decoder
Then, Conditional Logic

## Slide 114
Multicycle Control: Decoder

## Slide 115
Multicycle Control: Decoder
Decoder

## Slide 116
Multicycle Control: Decoder
ALU Decoder and PC Logic same as single-cycle

## Slide 117
Multicycle Control: Instr Decoder
RegSrc0 = (Op == 102)
RegSrc1 = (Op == 012)
ImmSrc1:0 = Op
Instruction | Op | Funct5 | Funct0 | RegSrc0 | RegSrc1 | ImmSrc1:0
LDR | 01 | X | 1 | 0 | X | 01
STR | 01 | X | 0 | 0 | 1 | 01
DP immediate | 00 | 1 | X | 0 | X | 00
DP register | 00 | 0 | X | 0 | 0 | 00
B | 10 | X | X | 1 | X | 10

## Slide 118
Multicycle ARM Processor

## Slide 119
Multicycle Control: Main FSM
Decoder

## Slide 120
Main Controller FSM: Fetch

## Slide 121
Main Controller FSM: Decode

## Slide 122
Main Controller FSM: Address

## Slide 123
Main Controller FSM: Read Memory

## Slide 124
Multicycle ARM Processor

## Slide 125
Main Controller FSM: LDR

## Slide 126
Main Controller FSM: STR

## Slide 127
Main Controller FSM: Data-processing

## Slide 128
Main Controller FSM: Data-processing

## Slide 129
Multicycle Controller FSM

## Slide 130
Multicycle Control
First, discuss Decoder
Then, Conditional Logic

## Slide 131
Multicycle Control: Cond. Logic

## Slide 132
Single-Cycle Conditional Logic

## Slide 133
Multicycle Conditional Logic
PCWrite asserted in Fetch state
ExecuteI/ExecuteR state:
CondEx asserts
ALUFlags generated
ALUWB state:
Flags updated
CondEx changes
PCWrite, RegWrite, and
MemWrite don’t see
change till new
instruction (Fetch state)

## Slide 134
Instructions take different number of cycles.
Multicycle Processor Performance

## Slide 135
Multicycle Controller FSM

## Slide 136
Instructions take different number of cycles:
  3 cycles:
  4 cycles:
  5 cycles:
Multicycle Processor Performance

## Slide 137
Instructions take different number of cycles:
  3 cycles: B
  4 cycles: DP, STR
  5 cycles: LDR
Multicycle Processor Performance

## Slide 138
Instructions take different number of cycles:
  3 cycles: B
  4 cycles: DP, STR
  5 cycles: LDR
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% data processing
Multicycle Processor Performance

## Slide 139
Instructions take different number of cycles:
  3 cycles: B
  4 cycles: DP, STR
  5 cycles: LDR
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% data processing
Average CPI = (0.13)(3) + (0.52 + 0.10)(4) + (0.25)(5) = 4.12
Multicycle Processor Performance

## Slide 140
Multicycle critical path:
Assumptions:
  RF is faster than memory
  writing memory is faster than reading memory
Tc2 = tpcq + 2tmux + max(tALU + tmux, tmem) + tsetup
Multicycle Processor Performance

## Slide 141
Tc2 = ?
Multicycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Decoder | tdec | 70
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 142
Tc2 = tpcq + 2tmux + max[tALU + tmux, tmem] + tsetup
= [40 + 2(25) + 200 + 50] ps = 340 ps
Multicycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Decoder | tdec | 70
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 143
For a program with 100 billion instructions executing on a multicycle ARM processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc2 = 340 ps
Execution Time = ?
Multicycle Performance Example

## Slide 144
For a program with 100 billion instructions executing on a multicycle ARM processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc2 = 340 ps
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(340 × 10-12)
= 140 seconds
Multicycle Performance Example

## Slide 145
For a program with 100 billion instructions executing on a multicycle ARM processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc2 = 340 ps
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(340 × 10-12)
= 140 seconds
This is slower than the single-cycle processor (84 sec.)
Multicycle Performance Example

## Slide 146
Review: Single-Cycle ARM Processor

## Slide 147
Review: Multicycle ARM Processor

## Slide 148
Aim to really improve performance
Use temporal parallelism
Divide single-cycle processor into 5 stages:
  Fetch
  Decode
  Execute
  Memory
  Writeback
Add pipeline registers between stages
Pipelined ARM Processor

## Slide 149
Single-Cycle vs. Pipelined

## Slide 150
Pipelined Processor Abstraction

## Slide 151
Single-Cycle & Pipelined Datapath

## Slide 152
WA3 must arrive at same time as Result
Register file written on falling edge of CLK
Corrected Pipelined Datapath

## Slide 153
Remove adder by using PCPlus4F after PC has been updated to PC+4
Optimized Pipelined Datapath

## Slide 154
Same control unit as single-cycle processor
Control delayed to proper pipeline stage
Pipelined Processor Control

## Slide 155
When an instruction depends on result from instruction that hasn’t completed
Types:
  Data hazard: register value not yet written back to register file
  Control hazard: next instruction not decided yet (caused by branch)
Pipeline Hazards

## Slide 156
Data Hazard

## Slide 157
Insert NOPs in code at compile time
Rearrange code at compile time
Forward data at run time
Stall the processor at run time
Handling Data Hazards

## Slide 158
Insert enough NOPs for result to be ready
Or move independent useful instructions forward
Compile-Time Hazard Elimination

## Slide 159
Data Forwarding

## Slide 160
Data Forwarding
Check if register read in Execute stage matches register written in Memory or Writeback stage
If so, forward result

## Slide 161
Data Forwarding

## Slide 162
Data Forwarding
Execute stage register matches Memory stage register?
Match_1E_M = (RA1E == WA3M)
Match_2E_M = (RA2E == WA3M)
Execute stage register matches Writeback stage register?
Match_1E_W = (RA1E == WA3W)
Match_2E_W = (RA2E == WA3W)
If it matches, forward result:
if (Match_1E_M • RegWriteM) ForwardAE = 10;
else if (Match_1E_W • RegWriteW) ForwardAE = 01;
else ForwardAE = 00;

## Slide 163
Data Forwarding
Execute stage register matches Memory stage register?
Match_1E_M = (RA1E == WA3M)
Match_2E_M = (RA2E == WA3M)
Execute stage register matches Writeback stage register?
Match_1E_W = (RA1E == WA3W)
Match_2E_W = (RA2E == WA3W)
If it matches, forward result:
if (Match_1E_M • RegWriteM) ForwardAE = 10;
else if (Match_1E_W • RegWriteW) ForwardAE = 01;
else ForwardAE = 00;
ForwardBE same but with Match2E

## Slide 164
Stalling

## Slide 165
Stalling

## Slide 166
Stalling Hardware

## Slide 167
Is either source register in the Decode stage the same as the one being written in the Execute stage?
Match_12D_E = (RA1D == WA3E) + (RA2D == WA3E)
Is a LDR in the Execute stage AND Match_12D_E?
ldrstall = Match_12D_E • MemtoRegE
StallF = StallD = FlushE = ldrstall
Stalling Logic

## Slide 168
B:
  branch not determined until the Writeback stage of pipeline
  Instructions after branch fetched before branch occurs
  These 4 instructions must be flushed if branch happens
Writes to PC (R15) similar
Control Hazards

## Slide 169
Control Hazards
Branch misprediction penalty
number of instruction flushed when branch is taken (4)
May be reduced by determining BTA earlier

## Slide 170
Early Branch Resolution
Determine BTA in Execute stage
  Branch misprediction penalty = 2 cycles
Hardware changes
  Add a branch multiplexer before PC register to select BTA from ALUResultE
  Add BranchTakenE select signal for this multiplexer (only asserted if branch condition satisfied)
  PCSrcW now only asserted for writes to PC

## Slide 171
Pipelined processor with Early BTA

## Slide 172
Control Hazards with Early BTA

## Slide 173
PCWrPendingF = 1 if write to PC in Decode, Execute or Memory
PCWrPendingF = PCSrcD + PCSrcE + PCSrcM
Stall Fetch if PCWrPendingF
StallF = ldrStallD + PCWrPendingF
Flush Decode if PCWrPendingF OR PC is written in Writeback OR branch is taken
FlushD = PCWrPendingF + PCSrcW + BranchTakenE
Flush Execute if branch is taken
FlushE = ldrStallD + BranchTakenE
Stall Decode if ldrStallD (as before)
StallD = ldrStallD
Control Stalling Logic

## Slide 174
ARM Pipelined Processor with Hazard Unit

## Slide 175
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% data processing
Suppose:
  40% of loads used by next instruction
  50% of branches mispredicted
What is the average CPI?
Pipelined Performance Example

## Slide 176
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% data processing
Suppose:
  40% of loads used by next instruction
  50% of branches mispredicted
What is the average CPI?
  Load CPI = 1 when not stalling, 2 when stalling
    So, CPIlw = 1(0.6) + 2(0.4) = 1.4
  Branch CPI = 1 when not stalling, 3 when stalling
  So, CPIbeq = 1(0.5) + 3(0.5) = 2
  Average CPI = (0.25)(1.4) + (0.1)(1) + (0.13)(2) + (0.52)(1) = 1.23
Pipelined Performance Example

## Slide 177
Pipelined processor critical path:
Tc3 = max [
tpcq + tmem + tsetup Fetch
2(tRFread + tsetup ) Decode
tpcq + 2tmux + tALU + tsetup Execute
tpcq + tmem + tsetup Memory
2(tpcq + tmux + tRFwrite) ] Writeback
Pipelined Performance

## Slide 178
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60
Register file write | tRFwrite | 70
Cycle time: Tc3 = ?
Pipelined Performance Example

## Slide 179
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60
Register file write | tRFwrite | 70
Cycle time: Tc3 = 2(tRFread + tsetup )
= 2[100 + 50] ps = 300 ps
Pipelined Performance Example

## Slide 180
Program with 100 billion instructions
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(1.23)(300 × 10-12)
= 36.9 seconds
Pipelined Performance Example

## Slide 181
Processor | Execution Time (seconds) | Speedup (single-cycle as baseline)
Single-cycle | 84 | 1
Multicycle | 140 | 0.6
Pipelined | 36.9 | 2.28
Processor Performance Comparison

## Slide 182
Deep Pipelining
Micro-operations
Branch Prediction
Superscalar Processors
Out of Order Processors
Register Renaming
SIMD
Multithreading
Multiprocessors
Advanced Microarchitecture

## Slide 183
10-20 stages typical
Number of stages limited by:
  Pipeline hazards
  Sequencing overhead
  Power
  Cost
Deep Pipelining

## Slide 184
Decompose more complex instructions into a series of simple instructions called micro-operations (micro-ops or µ-ops)
At run-time, complex instructions are decoded into one or more micro-ops
Used heavily in CISC (complex instruction set computer) architectures (e.g., x86)
Used for some ARM instructions, for example:
Complex Op Micro-op Sequence
LDR R1, [R2], #4 LDR R1, [R2]
ADD R2, R2, #4
Without u-ops, would need 2nd write port on the register file
Micro-operations

## Slide 185
Allow for dense code (fewer memory accesses)
Yet preserve simplicity of RISC hardware
ARM strikes balance by choosing instructions that:
  Give better code density than pure RISC instruction sets (such as MIPS)
  Enable more efficient decoding than CISC instruction sets (such as x86)
Micro-operations

## Slide 186
Guess whether branch will be taken
  Backward branches are usually taken (loops)
  Consider history to improve guess
Good prediction reduces fraction of branches requiring a flush
Branch Prediction

## Slide 187
Ideal pipelined processor: CPI = 1
Branch misprediction increases CPI
Static branch prediction:
  Check direction of branch (forward or backward)
  If backward, predict taken
  Else, predict not taken
Dynamic branch prediction:
  Keep history of last several hundred (or thousand) branches in branch target buffer, record:
    Branch destination
    Whether branch was taken
Branch Prediction

## Slide 188
MOV R1, #0 ; R1 = sum
MOV R0, #0 ; R0 = i
FOR ; for (i=0; i<10; i=i+1)
CMP R0, #10
BGE DONE
ADD R1, R1, R0 ; sum = sum + i
ADD R0, R0, #1
B FOR
DONE
Branch Prediction Example

## Slide 189
Remembers whether branch was taken the last time and does the same thing
Mispredicts first and last branch of loop
1-Bit Branch Predictor

## Slide 190
Only mispredicts last branch of loop
2-Bit Branch Predictor

## Slide 191
Multiple copies of datapath execute multiple instructions at once
Dependencies make it tricky to issue multiple instructions at once
Superscalar

## Slide 192
Ideal IPC: 2
Actual IPC: 2
Superscalar Example

## Slide 193
Superscalar with Dependencies
Ideal IPC: 2
Actual IPC: 6/5 = 1.2

## Slide 194
Looks ahead across multiple instructions
Issues as many instructions as possible at once
Issues instructions out of order (as long as no dependencies)
Dependencies:
  RAW (read after write): one instruction writes, later instruction reads a register
  WAR (write after read): one instruction reads, later instruction writes a register
  WAW (write after write): one instruction writes, later instruction writes a register
Out of Order Processor

## Slide 195
Instruction level parallelism (ILP): number of instruction that can be issued simultaneously (average < 3)
Scoreboard: table that keeps track of:
  Instructions waiting to issue
  Available functional units
  Dependencies
Out of Order Processor

## Slide 196
LDR R8, [R0, #40]
ADD R9, R8, R1
SUB R8, R2, R3 Ideal IPC: 2
AND R10, R4, R8 Actual IPC: 6/4 = 1.5
ORR R11, R5, R6
STR R7, [R11, #80]
Out of Order Processor Example

## Slide 197
LDR R8, [R0, #40]
ADD R9, R8, R1
SUB R8, R2, R3 Ideal IPC: 2
AND R10, R4, R8 Actual IPC: 6/3 = 2
ORR R11, R5, R6
STR R7, [R11, #80]
Register Renaming

## Slide 198
Single Instruction Multiple Data (SIMD)
  Single instruction acts on multiple pieces of data at once
  Common application: graphics
  Perform short arithmetic operations (also called packed arithmetic)
For example, add eight 8-bit elements
SIMD

## Slide 199
Multithreading
  Word processor: thread for typing, spell checking, printing
Multiprocessors
  Multiple processors (cores) on a single chip
Advanced Architecture Techniques

## Slide 200
Process: program running on a computer
  Multiple processes can run at once: e.g., surfing Web, playing music, writing a paper
Thread: part of a program
  Each process has multiple threads: e.g., a word processor may have threads for typing, spell checking, printing
Threading: Definitions

## Slide 201
One thread runs at at at a time
When one thread stalls (for example, waiting for memory):
  Architectural state of that thread stored
  Architectural state of waiting thread loaded into processor and it runs
  Called context switching
Appears to user like all threads running simultaneously
Threads in Conventional Processor

## Slide 202
Multiple copies of architectural state
Multiple threads active at once:
  When one thread stalls, another runs immediately
  If one thread can’t keep all execution units busy, another thread can use them
Does not increase instruction-level parallelism (ILP) of single thread, but increases throughput
Intel calls this “hyperthreading”
Multithreading

## Slide 203
Multiple processors (cores) with a method of communication between them
Types:
  Homogeneous: multiple cores with shared main memory
  Heterogeneous: separate cores for different tasks (for example, DSP and CPU in cell phone)
  Clusters: each core has own memory system
Multiprocessors

## Slide 204
Patterson & Hennessy’s: Computer Architecture: A Quantitative Approach
Conferences:
  www.cs.wisc.edu/~arch/www/
  ISCA (International Symposium on Computer Architecture)
  HPCA (International Symposium on High Performance Computer Architecture)
Other Resources